## Slide 1
Mission Overview
Mission Description: DSCOVR is a reimbursable project funded by the National Oceanic and Atmospheric Administration (NOAA) with a Launch vehicle being contributed by the United States Air Force (USAF). DSCOVR provides space weather measurements of the solar wind magnetic field, and the solar wind plasma ion velocity and density. These measurements provide warnings of space weather events with 15-60 minute lead times. DSCOVR also provides measurements of Earth radiances and imagery in the visible, NIR, and UV spectrum.
Organizations: NASA GSFC, NOAA, Air Force
Mission Overview: 3-axis stabilized spacecraft, in Lissajous orbit around the Earth-Sun L1 point, 1.5 million km from Earth.
Dry Mass: 425 kg
Wet Mass: 570 kg
Power: 500W EOL
Instruments:
Plasma – Magnetometer (PlasMag)
  Magnetometer
  Faraday Cup
  Electron Spectrometer
Earth Polychromatic Imaging Camera (EPIC)
NIST Advanced Radiometer (NISTAR)
Mission Data:
Launch Vehicle: Falcon 9 - USAF Provided
Launch Date: Feb 11, 2015
Orbit: L1 Lissajous
Mission Class: Category 2, Risk Class D

## Slide 2: DSCOVR Earth Science
EPIC Status
  RGB images posted daily at http://epic.gsfc.nasa.gov
  Level 1 A, B data posted at Langley ASDC (https://eosweb.larc.nasa.gov/ )
  In-flight calibrations completed
  Dark field corrections completed
  Stray light correction analysis completed
  Absolute calibrations established and continuously updated
  Level 2 data products generated and published at ASDC
  Instrument performs nominally
Earth Polychromatic Imaging Camera (EPIC) Objectives
Image the sunlit disk of Earth to form true-color RGB pictures of the planet with a spatial resolution of 35 km or better at the near the image center with 4 hour cadence. We achieve 10 km
Image Earth in ten spectral bands that are sufficient to determine ozone, aerosol, scene reflectivity, cloud cover and height, and vegetation indices. We achieved all of these
NIST Advanced Radiometer (NISTAR) Objectives
NISTAR will provide measurements that could be used to determine the Earth reflected irradiance in the wavelength range of 0.2-100 microns with an accuracy of 1.5% or better. We are still working on this problem
NISTAR Status
In-flight calibrations complete
Absolute calibration analysis continuing
Level 1 A, B data published at Langley ASDC
  Instrument performed nominally
Right: 30 cm Cassegrain Telescope
EPIC measures radiances from the sunlit face of the Earth on a 2048 x 2048 pixel CCD in 10 narrowband channels (UV, Visible, NIR) 317.5 to 799 nm.
Right: NISTAR measures the absolute “irradiance” integrated over the entire sunlit face of the Earth in 4 broadband channels.

## Slide 3
DSCOVR Level-1 Requirements
DSCOVR will utilize the EPIC instrument to image Earth in ten spectral bands that can be used to determine:
  Ozone
  Sulfur Dioxide
  Aerosol
  Cloud
  Vegetation
  RGB pictures of the planet with a spatial resolution of 35 km or better at central meridian (updated at KDP-E).
The time cadence of these spectral band images from EPIC will be provided on a best effort basis given existing ground system and network capabilities, and will typically be no faster than 10 spectral bands every 4 hours.
DSCOVR will utilize the NISTAR instrument to provide measurements that could be used to determine the Earth reflected irradiance in the wavelength range of 0.2 – 100 microns with an accuracy of 1.5% or better.

## Slide 4: EPIC Wavelengths and Science Products
Double Filter Wheel

## Slide 5
Processing step | Average impact | Affected pixels impact
Dark correction | Moderate | Extreme
Enhanced pixel detection | Small | Large
Read wave correction | Small | Small
Latency correction | Moderate | Significant
Non-linearity correction | Small | Small
Temperature correction | Small | Small
Conversion to count rates | Small | Small
Flat fielding | Significant | Large
Stray light correction | Significant | Large
Conversion to radiances | Significant | Significant
EPIC Level-1a Processing Steps
The highest impact corrections summarized on next slides.

## Slide 6
Dark current rates are inherent detector pixel level signals produced by thermal electrons during the integration time of the observation.
Pre-launch dark rate map based on a CCD temperature of -40°C, but in-flight temperature approximately -20°C.
Dark Corrections
Currently used constant dark rate map updated based on the images taken routinely in-flight. Significantly reduces error in dark correction. <1% effect for dark scenes.
Slope and oscillations will be corrected for summer 2018 reprocessing. Largely
due to temperature variations not fully characterized during pre-launch testing.
Will reduce the associated error to <0.5%.
??????

## Slide 7
EPIC flat field corrections are required due to 3 physical sources:
  Etaloning, filters 7 to 10 (>600nm) only
  Detector inhomogeneity, effect increases towards lower wavelengths
  Pixel response non uniformity, same effect for all filters
Pre-launch calibrations used for initial correction and updated based on in-flight observations.
Images below show pre-launch correction levels.
Flat Fielding

## Slide 8
Flat Fielding In-flight Updates
In-flight observations used to validate and improve flat fielding correction.
Implemented technique similar to MODIS where Earth observations averaged together to obtain a smooth image, taking advantage of atmospheric and surface features averaging out over the detector.
Any remaining features in these averaged maps would be attributed to:
  residual flat field errors,
  systematic features in the images, which always occur at the same place on the CCD.
Images below show residual differences between pre-launch and in-flight flat field correction.

## Slide 9
Stray Light Correction
Stray light is generated by in-field and out-of-field objects whose light is scattered within the EPIC optical system into un-wanted field angles. In essence, light from one part of the scene is corrupting measured signal from another part.
For visible filters the stray light error is large due to the larger dynamic range (50:1) in the data and larger amount of stray light induced by EPIC.
The “stray light error” shown here is based on the assumption that the data after the stray light correction are the “truth”.
Most affected by stray light are dark scenes (low albedo, clear sky), which have overestimated signal if no stray light correction is applied.
No correction, SL=1.94%
With correction, SL=0.09%
688nm

## Slide 10
Stray Light Correction (Cont.)
The quality of corrections was checked against MODIS measurements (whether EPIC data, multiplied with a single calibration value, agree with MODIS data (>400 nm) or OMPS (< 400 nm) for both clear sky and cloudy data).
For visible light filters (443, 551, 688, and 780 nm), where comparison with MODIS was possible, the stray light correction is a demonstrated improvement.
Counts
Radiance

## Slide 11
Level 1a,b: EPIC Geolocation
Analytical Correction
  Astronomical
  Optical Model
  Atmospheric Correction
Empirical Correction
  Attitude Accuracy Improvement
  Optical Calibration
Result
  Latitude, Longitude, sun & spacecraft values
  Accurate within +/- 0.5 pixel

## Slide 12
EPIC Level 2 Data Products
Data Product | Start | End | % Complete
Ozone | 2015 6/17 | 2018 6/18 | 92%
Sulfur Dioxide | 2015 12/3 | 2018 7/4 | Event Based
UV Aerosol | 2015 6/27 | 2018 7/11 | 98%
Cloud | 2015 8/18 | 2018 6/5 | 96%
Visible Aerosol, Atmospheric Correction, Surface Reflectance | 2015 6/13 | 2018 5/15 | 100%
Vegetation | 2015 7/11 | 2018 5/15 | 100%
O3SO2AI K. Yang | 2015 6/12 | 2018 7/12 | 100%
All EPIC Level 2 data is publicly available through Langley ASDC and EarthDATA.

## Slide 13
Req. 1a: Total Ozone - EPIC vs. MERRA-2
Comparison of EPIC total column ozone with the MERRA-2 assimilation ozone model for April 17, 2016.
Courtesy of J. Herman
317.5
325
340
388
443
551
680
687.75
764
779.5
Spectral Bands Used (nm)

## Slide 14
Req. 1a: Comparison of EPIC Total Column Ozone (TCO) with OMI TCO
Solid lines = 10 day Average
Grey = All EPIC data
Blue = All OMI Data
Units: DU = 2.69 x 1016 molecules/cm2
Location | EPIC Mean | OMI Mean | % Diff.
Seoul | 326 | 322 | 1.2
Busan | 312 | 307 | 1.6
Waterflow | 295 | 294 | 0.3
317.5
325
340
388
443
551
680
687.75
764
779.5
Spectral Bands Used (nm)
Courtesy of J. Herman

## Slide 15: Req. 1b: Volcanic Sulfur Dioxide Comparison: EPIC vs. SNPP-OMPS
This quantitative comparisons demonstrate a very good agreement of total SO2 mass measured by DSCOVR EPIC and SNPP OMPS. These maps also illustrate the advantages of EPIC: higher spatial resolution and more frequent observations, allowing improved monitoring of volcanic eruptions.
10:04 UTC
EPIC
11:52 UTC
EPIC
SO2 Mass=42 kt
SO2 Mass=41 kt
10:05 UTC
OMPS
SO2 Mass=45 kt
SO2 (DU)
Courtesy of K. Yang
317.5
325
340
388
443
551
680
687.75
764
779.5
Spectral Bands Used (nm)

## Slide 16
EPIC Hourly SO2 maps on June 17, 2018 from the June 16 volcanic eruption on Fernandina Island in the Galapagos (triangle).
Fast dispersion of volcanic plume with prevailing tropospheric winds.

## Slide 17
NPP/OMPS
AQUA/AIRS
EPIC: 21:54 UTC March 28. 2016
Req. 1b: Aerosols - Volcanic Sulfur Dioxide Comparison:
EPIC vs. NPP/OMPS and AQUA/AIRS
Courtesy of N. Krotkov
EPIC SO2 retrievals (a and b) for the high-latitude eruption of Pavlof (Alaska) in March 2016 under challenging viewing conditions.
Comparisons with the low-Earth orbiting Suomi NPP-hyperspectral Ozone Mapping & Profiler Suite (OMPS) SO2 data (c) and the atmospheric infrared sounder (AIRS) on NASA Aqua satellite shows that EPIC clearly detects the proximal volcanic plume where SO2 columns were highest (>10 Dobson Units: 1DU = 2.69x1016 molecules SO2 cm-2), along with some of the distal plume.
The total SO2 mass of 33 kilotons (kT) measured by AIRS compares favorably with the EPIC retrievals, which detected ~25 kT of SO2.
EPIC: 00:08 UTC March 29. 2016
317.5
325
340
388
443
551
680
687.75
764
779.5
Spectral Bands Used (nm)

## Slide 18
Req. 1c: UV Aerosols - Comparison of EPIC to OMI
Courtesy of O. Torres
317.5
325
340
388
443
551
680
687.75
764
779.5
Spectral Bands Used (nm)
EPIC
OMI

## Slide 19
Req. 1c: Aerosols - EPIC Above-Cloud-Aerosol Optical Depth (ACAOD)
Comparison with ORACLES-2 Lidar Observations
Courtesy of O. Torres
340
317.5
325
388
443
551
680
687.75
764
779.5
Spectral Bands Used (nm)

## Slide 20: Req. 1c: Aerosols - Retrieving aerosol layer height from EPIC O2 A and B bands Comparison with CALIOP Observations
A case study: EPIC at 2016-04-17 14:59 UTC
AOD
H, km
RGB
CALIPSO 2016-04-17 14:18 UTC
sun glint
removed
CALIPSO
track
EPIC retrieved H
clouds
EPIC retrieved H
Courtesy of Y. Yang
443
340
317.5
325
388
551
680
687.75
764
779.5
Spectral Bands Used (nm)
Notes: Retrieval results of AOD and aerosol height from EPIC O2-A and B bands
Validate with collocated CALIPSO measurements of backscatter and extinction coefficients.
Not an actual product, yet. We know that this is Saharan dust

## Slide 21
EPIC cloud mask validation example (a) EPIC RGB image taken on Aug. 18, 2016 at 08 GMT, (b) EPIC cloud mask and (c) cloud fraction of each EPIC pixel calculated from collocated Geo/Leo satellite products by NASA LRC. Comparison show that EPIC cloud mask performs well. It generally classifies a pixel as cloudy when the pixel has a cloud fraction above 0.3.
Courtesy of Y. Yang
Req. 1d: Cloud Cover - Cloud Mask
443
340
317.5
325
388
551
680
687.75
764
779.5
Spectral Bands Used (nm)

## Slide 22
EPIC cloud effective pressure and cloud optical thickness (COT) performance example. Comparison are done along a line in the middle of the image (a) comparison between EPIC A-band cloud pressure and the Geo/Leo composite; and (b) comparison between EPIC COT assuming liquid/ice with the Geo/Leo composites.
Results show that the EPIC average A-band pressure is 658 mb, while the Geo/Leo composite has a value 645mb. The average COT for EPIC assuming liquid and ice phases are 8.9 and 7.4, while the Geo/Leo composite has a value of 9.5. These results are consistent with the theoretical expectations
Courtesy of Y. Yang
Req. 1d: Cloud Height and Cloud Optical Depth
443
340
317.5
325
388
551
680
687.75
764
779.5
Spectral Bands Used (nm)

## Slide 23
Req. 1e: Vegetation Index and Atmospheric Correction
Monthly Composites of
RGB Surface BRF
NDVI
Courtesy of A. Lyapustin
Spectral bands used:
443, 551, 680, 780 nm
680
443
340
317.5
325
388
551
687.75
764
779.5
Spectral Bands Used (nm)

## Slide 24
max: 4.9 105
SLOPE, DEG
Req. 1e: Sunlit Leaf Area Index
First product to show sunlit leaf area index of illuminated leaves
Notes: First product to show sunlit leaf area index of illuminated leaves

## Slide 25
Sensor | Green spectral band, nm | 
 | Center | Band width
MISR | 555 | 20
EPIC | 551 | 3
Courtesy of Y. Knyazikhin
20160823152458
Mean MISR and EPIC BRFs over an area of 563kmx985km in Amazonian rainforests, which represents structurally homogeneous area.
Req. 1e: Vegetation and BRF – EPIC vs. MISR
680
443
340
317.5
325
388
551
687.75
764
779.5
Spectral Bands Used (nm)
Notes: Date: 2016-08-23, 15:24:58GMT. Shown are mean MISR and EPIC BRFs over an area of 563kmx985km in Amazonian rainforests, which represents structurally homogeneous area.

## Slide 26
R2=0.66
R2=0.71
R2=0.74
R2=0.31
R2=0.51
R2=0.63
EPIC Land Cover Map
Courtesy of Y. Knyazikhin
Req. 1e: Leaf Area Index – Comparison with C6 MODIS (Aug 2016)
680
443
340
317.5
325
388
551
687.75
764
779.5
Spectral Bands Used (nm)
Notes: Spectra bands used to derived the VESDR product: 551nm, 680nm and 780nm.
EPIC Land Cover Map was derived from MODIS 8-biome 500 m Land cover type 3 product (MCDLCHKM). This static map is input for VESDR algorithm, which will be released to users. Global vegetation is stratified into eight canopy architectural types, or biomes. The eight biomes are
B1: grasses and cereal crops,
B2: shrubs,
B3: broadleaf crops,
B4: savannas,
B5: evergreen broadleaf forests,
B6: deciduous broadleaf forests,
B7: evergreen needle leaf forests,
B8: deciduous needle leaf forests.
------------------------------------------------------
Shown are histograms of EPIC LAI and C6 MODIS LAI products for different biome types.
B6: A low R2 for is due to biome mixture at 10 km EPIC pixel: MODIS LAI product is at 500m resolution. Biome mixture within 500m pixel is low and thus MODIS gives accurate LAI for B6. In the case of EPIC, biome mixture within 10 km is high at low LAIs. Thus EPIC histogram includes both B6 and other biomes at low LAIs. Distribution of biome types within each 10 km pixels is also a product of the VESDR and will be available to users.
B5: same as for B6.
B3: may indicate a bias of 0.25 LAI units.
B1: I believe that EPIC provides a more accurate LAI histogram.

## Slide 27
New Product: UV 388 nm Reflectivity (Clouds + Snow or Ice)
Reflectivity 0 < R < 1
Brighter Clouds are usually at higher altitude
In the UV, the land and ocean have a reflectivity of 0.04 or less, so the reflectivity is mostly clouds and snow/ice.
The ground is not visible.
Notice Greenland in upper right
Allows investigation of diurnal variation.
08/23/2017 17:54:36

## Slide 28
New: UV Erythemal Irradiance (Watts/m2 and UV Index)
UV index = 40* I(Watts/m2)
A UV index of 10 is quite dangerous for sunburn and cancer
Note the high values in the Andes mountains UV index 16 to 20
Erythemal Irradiance from sunrise (West) to sunset (East)
Calculated from measured ozone amounts and cloud reflectivity

## Slide 29
20160317094607
Many DSCOVR/EPIC images contain bright flashes of light over both ocean and land. It was demonstrated that the flashes over land are specular reflections off tiny ice platelets floating in the air nearly horizontally. Such deep space detection of tropospheric ice can be used to constrain the likelihood of oriented crystals and their contribution to Earth albedo.
Source: Marshak et al., 2017. Terrestrial glint seen from deep space: oriented ice crystals detected from the Lagrangian point. Geoph. Res. Lett., 44, doi:10.1002/2017GL073248.
20160317094609
zoom
20151028094609
20151028094609
zoom
Glint from oriented ice crystals

## Slide 30
Two EPIC NDVIs from March 22, 2016
If the EPIC O2 B-band (688 nm) is used instead of the red band, the effect of atmosphere (the diffuse radiation) on surface reflectance will be reduced and the residual uncertainties in atmospheric correction can be better tolerated. This is due to two factors:
vegetated surface is yet sufficiently dark at 688 nm and
the O2 absorbing atmosphere substantially reduces multiple scattering.
Source: Marshak, A. and Y. Knyazikhin, 2017: The spectral invariant approximation within canopy radiative transfer to support the use of the EPIC/DSCOVR oxygen B-band for monitoring vegetation. J. Quant. Spectrosc. Radiat. Trans., 191, 7-12, doi:10.1016/j.jqsrt.2017.01.015.

## Slide 31
30 June 2015
EPIC
Google
Earth
Pixel Projection = 1 arc second = 8 km
Near the Sub-Satellite Point
Requirement 1g: 35 km resolution at central meridian
Features 10 km resolvable due to the combination of RGB images.

## Slide 32
Days from June 12, 2015
2015
2016
2017
2018
Req. 2: Time Cadence of EPIC RGB Images
Goal: 6 per day
Ops plan:
13 during winter
22 during summer
Performance:
2016: 90.0%
2017: 92.4%
2018: 92.2%
Total number of images:
15,406 out of 17,006
Total # lost due to spacecraft safe-hold:
347 or 2% loss
Spacecraft Safe-Hold Events
Number of EPIC RGB images per day

## Slide 33
https://epic.gsfc.nasa.gov

## Slide 34: DSCOVR: NISTAR
Band | Wavelength
Total | 0.2 µm to 100 µm
SW Solar Reflected | 0.2 µm to 4 µm
NIR Solar Reflected | 0.7 µm to 100 µm
Photodiode | 0.2 µm to 1.1 µm
Full-disk measurement of absolute out-going irradiance
Three Electrical Substitution Radiometers in different bands
Cavity absorbers and electrical substitution utilized for excellent long-term stability
One Silicon Photodiode Channel

## Slide 35
Filter Channel | Instrument Noise (Precision) |  |  | Responsivity (Calibration) |  | NISTAR Total Uncertainty5
 | Space View1 | Earth View2 | Total Noise | Laboratory Calibration3 | Stability on Orbit4 | 
 |  | 4 Hr Daily | 4 Hr Daily |  |  | 4 Hr Daily
Total | 1.0 % | 0.7 % 0.3 % | 1.2 % 1.0 % | <0.2 % | 0.3 % | 1.3 % 1.1 %
SW | 1.3 % | 1.0 % 0.4 % | 1.7 % 1.4 % | 1 % | 0.3 % | 2.0 % 1.7 %
NIR | 3.5 % | 4.2 % 1.7 % | 5.5 % 3.9 % | 1 % | 0.3 % | 5.6 % 4.0 %
Normalized to the Earth signal. 2-hour dark space view performed monthly. 3 consecutive dark space views are averaged for the SW and NIR channels; no averaging for the Total channel.
Based on the 4-hour and daily averages of the Earth view signal.
Uncertainty components are from both the ESR receiver and the filter transmission. For the two filtered channels, SW and NIR, the uncertainty of the filter transmission dominates.
From on-orbit inter-comparison between receivers and filters collected while viewing the earth.
Total uncertainties of 4-hour and daily include both the measurement precision and calibration.
DSCOVR: NISTAR – Uncertainty Budget
All uncertainties are calculated at k = 1

## Slide 36
DSCOVR: NISTAR Photodiode for 2.5 years
NISTAR PD Channel over 2.5 years
Earth distance effects removed
DISCOVR orbit effects viewing angle which does not align with seasons
Observed shortwave reflectance shows significant annual variations (5 % to 8%).

## Slide 37
DSCOVR: NISTAR PD - SW - EPIC Comparison
NISTAR PD/SW Compared to EPIC
Data averaged over a weekly time period
EPIC spectral radiance is weighted sum of 10 bands to match the PD response
Long-term variations agree well in spite different spectral response of NISTAR SW and PD

## Slide 38
DSCOVR: NISTAR-CERES SW Comparison
NISTAR SW & PD Versus CERES SW SYN1deg
Stable short-term correlations
NISTAR SW and PD both show larger (≈20%) daily variations than CERES Synoptic Model
NISTAR SW shifted down by 12 % for comparison

## Slide 39
DSCOVR: NISTAR-CERES SW Comparison
NISTAR and CERES SW Comparison (weekly average)
Anisotropy factor removes most scene angular dependence
Resultant NISTAR SW flux is higher than CERES SW flux by 12 %

## Slide 40: DSCOVR: NISTAR Conclusions
NISTAR Ground Calibration and “Native Scale” agreed to < 1 %
No Degradation On-Orbit
  Cavity Responsivities < 1 %.
  Filter transmittance stable to < 0.3 % and within 1 % of expected value
CERES Synoptic Model using LaRC anisotropy predictions disagree with SW and LW by ≈10 %
Both teams continue to work the disagreement.
NISTAR is a very “clean” measurement, but inter-comparisons with other instruments are highly model dependent.

## Slide 41
Summary
EPIC Level 1, 2 data products exceeded the mission level 1 requirements.
EPIC RGB image resolution and cadence exceeded level 1 requirements.
NISTAR A-band (full bandwidth) data product reached the required 1.5% precision requirement.
Comparison of NISTAR and CERES short and long wavelength products is on-going and presents some puzzles.