## Slide 1: DSCOVR Earth Science Processing 3/31/2015
Karin Blank

## Slide 2: Group/Meeting Purpose
Science processing related issues
  Facilities
  Data availability
  Data access
Data
  Formats
  Ancillary
  Archival
Science?

## Slide 3: Current status
Spacecraft
  No major issues to report
EPIC
  Functional test
  Starting to take/send dark current images for calibration
NISTAR
  Functional test
Processing
  Level 0 data is being processed and forwarded to the ASDC archive
Other
  EPIC & NISTAR level 1 Data format control books are in CCR process

## Slide 4: Upcoming activities
Date | Milestone
Late May/Early June | NISTAR Calibration
June 7 | Orbit Insertion
June 9 – Early July | Instrument Commissioning
Late August | Level 1 data available

## Slide 5: Level 1 Science processing

## Slide 6: TSOC->DSOC
TSOC
  Original Triana system was developed and worked on up until mid-2001
  Was hosted run out of Scripps, archive was GES-DISC
  Produced level 1, 2, 3, and RGB products
  System and software underwent standard reviews and testing at the time
  Initial configuration completed and running at time of shutdown
DSOC
  Reuses and modernized TSOC science software where possible
  Has updated science and processing pipeline components
  Processing is hosted at GSFC, archive is at ASDC Langley
  Produces level 1 and RGB products
  Has passed DSCOVR Ground Readiness Testing and is operational

## Slide 7: DSOC, level 0 & 1 processing
DSOC consists of 3 facilities
  Science and Planetary Operations Control Center (SPOCC)
    Telemetry ingest
    Level 0 processing
    Telemetry & process monitoring
  NASA Center for Climate Simulation (NCCS)
    Level 1 processing
  Atmospheric Science Data Center (ASDC)
    Science data archival & dissemination
DSOC is a virtual facility
  Operates within existing facilities
  Owns no equipment or hardware

## Slide 8: EPIC Level 1 Data Flow
CDAS Antenna
VC2-4 Day file
sftp transfer (once/day)
SPOCC
Level 0 processing
NCCS
Local
archive
Level 1 processing
ASDC
Science & public data distribution
~12H
2H
1H
3-8H
3H

## Slide 9: Data Flow, NISTAR
CDAS Antenna
VC0-1
once/day
SPOCC
Level 0 Processing
NCCS
Local
archive
ASDC
Science & public data distribution
SWPC
NGDC
Day files
1-5D
Level 1 processing

## Slide 10: EPIC Products
Product | Contents
EPIC Level 1A | Calibrated EPIC images All at 2048x2048, upscaled as required Geolocation grids per image Selenographic grids per image (when applicable) Instrument & geolocation metadata per image ~150MB/set
EPIC Level 1B | EPIC L1A images, georectified to common grid All at 2048x2048 Geolocation grids per set Sun and Spacecraft angles per set Instrument & geolocation metadata per set ~90MB/set
EPIC RGB | Red Green Blue composite image ~4MB/image

## Slide 11: NISTAR Products
Product | Contents
NISTAR Level 1A | Uncalibrated and calibrated data Calibration tables Geolocation information ~50 MB/set
NISTAR Level 1B | Summary data ~20 MB/set

## Slide 12: Data
Data formats
  Level 1 EPIC & NISTAR - HDF 5
  EPIC RGB - png
  Sample data available
Format Documentation
  EPIC Data Format Control Book
  NISTAR Data Format Control Book
Latency
  EPIC – 9am next day
  NISTAR – 1-5 days
Data access (via ASDC)
  http/ftp access (fast via GSFC internal, 8+MB/s)
  User help/services

## Slide 13: Level 2 Science Processing

## Slide 14: Facilities
There are no facilities available via the DSCOVR project
Level 2 processing options are
  Apply for NASA High-End computing facilities
    NASA Center for Climate Simulation (NCCS) @ GSFC
    NASA Advanced Super Computer (NAS) @ Ames
    http://www.hec.nasa.gov/request/process.html
  Organizational Facilities
  DIY

## Slide 15: NCCS
Being used for level 1 processing
Easy portability between local desktop and supercomputer
  Software can be run as interactive terminal or take advantage of supercomputer features (scheduling & multiple nodes)
Extensive software support
  Matlab
  IDL
  Intel Math Kernel Library
Help desk/User support

## Slide 16: Discussion
Processing plans
Ancillary data needs
  Spacecraft information?
  Other ancillary data?
Future topics
  Data formats
  Archival of level 2 processing
  ?

## Slide 17: Backup

## Slide 18: DSOC Responsibilities
EPIC
  Telemetry VC2-4 ingest (via CDAS)
  L0, L1A, L1B processing
  Archival & distribution via ASDC
  Science data monitoring
NISTAR
  Telemetry ingest VC0-1 (via SWPC)
  L0, L1A, L1B processing
  Archival & distribution via ASDC
Plasmag
  Telemetry ingest VC0-1 (via SWPC & NGDC)
  L0 Processing for calibration
  Local archival & access for project scientists

## Slide 19
MMFD
SWPC
(APS)
NGDC
Real-Time TLM
Real-Time TLM
Real-Time
TLM
TLM & Space
Weather Files
TLM Files
Tracking Data
Real-Time
CMD/TLM
TLM
TLM
CMD & TLM
CMD & TLM
Real-Time
CMD/TLM
Orbit Products
Acquisition Data
To All Stations
To SWPC
And DSOC
Launch Facility
I&T Facility
MOC
(bMOC)
EPIC Data
Ops products for validation and trend data
SDVF
DSOC
WCDAS
FCDAS (Backup)
CMD & TLM
CMD & TLM
Ground Segment Boundary
TDRSS
DSCOVR
FSW Updates
DSN
NEN
SN
SCaN Services
CDAS
RTSWnet
AFSCN
(L&EO, Ranging, Backup)
DSCOVR Ground Segment
Functional Block Diagram
PlasMag Calibration Results
Maneuver Plans
RGB Images
Public
Real-Time
CMD/TLM
TLM Files
Ranging
NOAA
NASA
Geomagnetic Storm Warnings
Level 1 and 2 Space Weather Products
Trend
Data
TLM Files
(VC0-VC4)
Space Weather Users

## Slide 20: DSOC Processing Architecture
CDAS
SWPC
NGDC
PlasMag Calibration Results
VC0-1 15 min Files
(PlasMag/NISTAR)
VC2-4 (EPIC)
VC0-1 Day Files (NISTAR/PlasMag)
ASDC
Researchers/Public
DSOC
Ingest (SPOCC)
Data Ingest
Parsing
Telemetry Monitoring
Plasmag data
EPIC/
NISTAR data
Science Team
MOC
MMFD
Predicted Ephemeris Data
DSCOVR T&C Database
DSCOVR Trended Data
Archive & Distribution
Processing
Process (NCCS)
Sensor Calibration
L1A
Geolocation
L1B

## Slide 21: Data Flow, EPIC
CDAS Antenna
VC2-4 Day file
sftp transfer (once/day)
SPOCC
Ingest
Parse
Level 0 data
NCCS
Local
archive
Calibrate, geolocate
Level 1a data
Georectify
Level 1b data
Color correct
RGB data
ASDC
Science & public data distribution
~12H
4-8H
1H
3-8H
3H

## Slide 22: Data Flow, NISTAR
CDAS Antenna
VC0-1
once/day
SPOCC
Ingest
Parse
Level 0 data
NCCS
Local
archive
Collate Science & Engineering data
Level 1a data
Summary/trending
Level 1b data
ASDC
Science & public data distribution
SWPC
NGDC
Day files
1-5D