## Slide 1: EPIC Geolocation
Karin Blank
NASA/GSFC Code 586
October 3rd, 2017

## Slide 2: Level 1 Products
Level 1A
Images are calibrated counts in native sensor format
Geolocation provides per pixel
  Latitude/Longitude coordinates
  Spacecraft viewing angles
  Sun angles
Level 1B
Images are georectified into a common reference frame
Geolocation in common reference frame
  Latitude/Longitude coordinates
  Spacecraft viewing angles
  Sun angles

## Slide 3: Algorithm Progress
Focus | Algorithm Version | Product Release Version | Features
Simulator | Revision 0 |  | Pre-launch simulator
Relative Geolocation | Revision 1 | Version 0 | First geolocation; website pictures
 | Revision 2 |  | Mitigation of issues with optical artifacts
 | Revision 3 |  | Improved cross-band registration
 | Revision 4 | Version 1 | Subpixel registration L1b (Kai Yang’s algorithm)
Absolute Geolocation | Revision 5 | Version 2 | Initial fixes for absolution geolocation
 | Revision 6 | Version 3 (future) | Atmospheric refraction correction, improved optical model, attitude correction

## Slide 4: Geolocation anatomy
Geographic Model
Telescope prescription
  Focal length (magnification)
  Optical distortion
Optical Model
Position of Earth
  Spacecraft attitude & ephemeris
  Astronomical
3D Earth description
  Geoid
  Terrain model
  Atmospheric refraction
Pose
2D Renderer
Lat/lon coordinates
View angles
Sun angles
Georectification

## Slide 5: Spacecraft Attitude in Triana - Star Tracker + EPIC
Star tracker
  Coarse attitude control
EPIC
  Fine attitude control onboard processing of imagery
  Abandoned since not needed for space weather requirements
EPIC Correction

## Slide 6: Spacecraft Attitude in DSCOVR– Star Tracker only
Star tracker
  Only coarse attitude control
Wandering pitch/yaw
Roll accuracy less than .5 degrees
  Images require minimum .05 degrees
R05
  Has basic pitch/yaw correction
  No roll correction

## Slide 7: Geolocation anatomy
Geographic Model
Telescope prescription
  Focal length (magnification)
  Optical distortion
Optical Model
Position of Earth
  Spacecraft attitude & ephemeris
  Astronomical
3D Earth description
  Geoid
  Terrain model
  Atmospheric refraction
Pose
2D Renderer
Lat/lon coordinates
View angles
Sun angles
Georectification

## Slide 8: EPIC Optical Design
EPIC Schematic
Field Lens Group
Field Lens Group
Primary
Secondary
CCD

## Slide 9: EPIC Optical Correction
Requires
  Focal Length
  Optical distortion
    Radial
    Tangential
  Chromatic aberration
    Transverse
R05
  Initial focal length correction
  No optical distortion correction
  No chromatic aberration correction
Example of pincushion distortion

## Slide 10: Problems for R06
Positional accuracy below requirements
  3 variables below needed accuracy
Possible time issue
  2 variables below needed accuracy
Undefined telescope prescription
  11+ variables with unknown values

## Slide 11: Solution – Forward/Back Propagation
2D XY Offset
3D XYZ Rotational Correction
Optical Distortion model
Initial Coarse Input
Modified Input
Equation
Results
Scoring
Basic XY Offset Detection
Astronomical/
Star Tracker
Best Guess

## Slide 12: Forward/Back Propagation
Forward Propagation
  Take coarse results and create a spread of different variations
  Draw variation results with EPIC simulator using MODIS imagery
  Score results against EPIC image
Back Propagation
  Take inputs used for best scoring image and put it back as coarse inputs into the algorithm
  Repeat forward propagation with finer variation
Algorithm teaches itself how to draw the EPIC image correctly, thereby deriving the correct geolocation solution

## Slide 13: Example
EPIC Image
Forward/Back Propagation

## Slide 14: R05 vs R06 – South Africa
R05
R06 (no optical correction)

## Slide 15: R05 vs R06 – Center of projection
R05
R06 (no optical correction)

## Slide 16: R05 vs R06 – India
R05
R06 (no optical correction)

## Slide 17: Status for R06
Corrections complete
  Atmospheric refraction
  2D XY Offset
  X rotational (time)
  Z rotational
In progress
  Optical distortion correction
  Chromatic aberration correction