## Slide 1: Improvement and Evaluation of Total O3 and Volcanic SO2 from DSCOVR EPIC
Kai Yang - UMCP
DSCOVR Science Team Meeting, GSFC Oct. 3 – 4, 2017
Acknowledgement: This work is supported by NASA.

## Slide 2: Evaluation of EPIC O3 Presented at Last DSCOVR STM
Significant O3 biases between EPIC and OMPS
total Ozone: ~11 DU or ~3 %

## Slide 3: Improvements
Soft calibration to correct UV radiance biases
Seasonal-dependent column-classified O3 climatology for more accurate O3 profile specification
Look-Up Tables (LUTs) for fast and accurate radiative transfer modeling
Spatial Optimal Estimation (SOE) for effective band-to-band mismatch correction

## Slide 4: Soft Calibration: UV bands
01/09/2017
10/15/2015
EPIC Band 1
317 nm
Imeas: sun normalized radiance measured by EPIC

## Slide 5: Soft Calibration: Time Dependence
01/09/2017
10/15/2015
vs.
No significant
Change over time

## Slide 6
Column-Classified O3 Climatology
By Month and Latitude Zones

## Slide 7: Accounting for O3 Profile Variations
Square root of the diagonal of the covariance matrix
Normalized covariance matrix: normalized by the product of the square root variance.
First two eigenvectors of the covariance matrix

## Slide 8: Fast and Accurate Radiance Modeling with Look-Up Tables
Accuracy ~ 0.2 % for full range of angles and O3
Processing speed-up by a factor of ~ 5.
Use heritage TOMS-like LUT approach may have a few % error.
LUT Radiances achieve an accuracy better than 0.2%
LUT with layer Jacobian

## Slide 9: Spatial Optimal Estimation (SOE)
O3
Δ O3
LER @ 340 nm
O3 (DU) ΔO3 (DU) LER @ 340 nm
Simultaneous O3 and reflectivity estimation to correct errors in O3 and reflectivity due to timing differences among observations from different bands, i.e., band-to-band scene mismatch. SOE reduces the O3 artificial noise level by ~ 5 DU.

## Slide 10: Inter-comparison of total O3 EPIC vs. MERRA-2
EPIC O3
MERRA-2 O3
Δ O3
EPIC O3 (DU) Merra-2 O3 (DU) ΔO3 (DU) = EPIC – MERRA2
2017-09-01T01:04:37Z

## Slide 11: Inter-comparison of total O3 EPIC vs. MERRA-2
2017-09-01T01:04:37Z
VZA <= 69°
Mean O3 : -1.7 DU
Std O3 : 7.7 DU

## Slide 12: Inter-comparison of total O3 EPIC vs. MERRA-2
EPIC O3
MERRA-2 O3
Δ O3
EPIC O3 (DU) Merra-2 O3 (DU) ΔO3 (DU) = EPIC – MERRA2
2015-10-15T09:48:18Z

## Slide 13: Inter-comparison of total O3 EPIC vs. MERRA-2
2015-10-15T09:48:18Z
VZA <= 69°
Mean O3 : -3.7 DU
Std O3 : 9.0 DU

## Slide 14: Total O3 EPIC vs. MERRA-2
EPIC O3
MERRA-2 O3
Δ O3
EPIC O3 (DU) Merra-2 O3 (DU) ΔO3 (DU) = EPIC – MERRA2
2015-10-15

## Slide 15: Ozone Summary
Good agreement between EPIC and MERRA-2 O3: their difference is characterized by the daily mean: better than 4 DU or 1.4%, and the daily standard deviation: 9 DU or 3.3% for VZA<69°.
This agreement is achieved with one set of calibration coefficients that are applied to the full EPIC record without change over time.
Reducing the systematic differences may require detector specific calibration coefficients.
In addition, better agreement may be achieved with more accurate retrievals under cloud and or aerosol conditions.

## Slide 16
SO2 (DU)
OMPS
OMPS
OMPS
EPIC
11:52 UT
11:04 UT
SO2 Mass
EPIC : 45 kt
OMPS: 55 kt
SO2 Height
Volcanic SO2 : OMPS vs. EPIC
Etna Eruption 12/03/2015

## Slide 17: Product Status
Total O3 accuracy is estimated to be better than 2% for SZA < 69° and SO2 accuracy is estimated to be better than 25% for column amount > 10 DU.
Ozone product has sufficient quality and accuracy to be released.