## Slide 1
SO2 and Ash Products from EPIC Observations
Principal Investigator: Nickolay Krotkov (GSFC 614)
Co-Investigators: Brad Fisher (SSAI), Can Li (UMCP ESSIC), Pawan K. Bhartia (NASA GSFC), Simon Carn (MTU), Eric Hughes (AOSC/UMCP);
Collaborators: Omar Torres (NASA GSFC), Fred Prata (NILU Norway), Steve Taylor (SSAI);
Simulated volcanic SO2 cloud from 2006 Soufriere Hills eruption
We proposed to implement our BUV algorithms previously developed for TOMS, OMI and OMPS to enable SO2 and Ash Index (AI) products from EPIC UV observations to demonstrate time resolved estimates of transient volcanic SO2 and ash clouds
Notes: Fig. 1. Simulation of the view of the Earth from DSCOVR’s EPIC sunrise to sunset observations showing that EPIC will enable unprecedented high-frequency coverage of volcanic plumes. In this example, a volcanic SO2 cloud from May 2006 Soufriere Hills eruption (Montserrat, West Indies) drifting across the Pacific, is captured seven times in one day by EPIC, assuming a 90 minute interval (22.5o rotation). The SO2 cloud is simulated based on actual OMI Level 3 0.25°×0.25° gridded data (about the same resolution as EPIC) with up to 15 DU of column SO2. The SO2 cloud is shown as the light colored feature against blue ocean background, after the plume had drifted eastward to a location just north of the equatorial Pacific.

## Slide 2
Background
SO2 Algorithm
Retrieved Parameters (SO2, O3, R and dRdλ)
SO2 Plume Evolution
  Comparisons with Other Satellites
  L1B Issues
  Product Status
  New Science Questions
Outline

## Slide 3
EPIC UV channels
317
325
340
388
SO2 O3 AI = N340m – N340calc(LER388)
Notes: Description of the DSCOVR/EPIC SO2 Algorithm PI: Nick Kroktov
The DSCOVR/EPIC volcanic SO2 algorithm is a modified version of the heritage NASA Total Ozone Mapping Spectrometer (TOMS) 4-band algorithm, adapted to the EPIC wavelengths. The algorithm uses all four EPIC UV channels (centered at 317nm, 325nm, 340 nm, 388nm) to retrieve 4 parameters of the state vector (x): vertical column amounts of SO2 (assuming 13km height) and total O3, the Lambertian equivalent reflectivity at 388 nm (R), and its spectral dependence, dR/d. The algorithm relies on spectral differences in SO2 and O3 absorption cross sections to separate the two trace gases. SO2 is more absorbing than O3 at the shortest UV channel (317 nm), whereas O3 is more absorbing at the longer channel (325nm).
The retrieval is performed iteratively for each EPIC pixel with SZA < 75o. It starts with the climatological profile of O3 and zero SO2 and first computes Lambertian equivalent scene Reflectivity (LER) at 388 nm (R). This parameter remains fixed during the iterations. The algorithm then retrieves adjustments to the state vector: Δx =[ΔSO2, ΔO3, Δ(dR/d)] by matching measured and calculated sun-normalized backscatterd UV (BUV) radiances at shorter spectral channels (317,325 and 340nm). The sensitivities (Jacobians) associated with linear perturbations in SO2, O3 and R are pre-computed for each UV spectral band and stored in look-up tables, which are numerically interpolated for EPIC viewing geometry and state vector values at each iteration. This algorithm appears to have adequate sensitivity to detect moderate to large volcanic eruptions from L1 Lagrange point.
EPIC channels shown in purple:
Major absorbing gases are :
Ozone (o3) always present; 90% in stratosphere; global average ~300DU;
317 – O3 and SO2
325 – ozone and SO2
SO2/O3 X section ratios are different at 317nm and 325nm allow separating O3 and So2 abundancies;

## Slide 4
EPIC SO2 Algorithm: Step 1
NM: Measured N= -100*log10(I/F), NC: Calculated N= -100*log10 (I/F)
dN/dSO2, dN/dO3, dN/dR represent sensitivities of N vrt SO2, O3 and Reflectivity.
MS_SO2 uses 4 UV DSCOVR/EPIC channels at 317.5, 325, 340 and 388nm to retrieve state vector containing 4-parameters: SO2, O3, R(λ=388nm) and dR/dλ
Compute Lambertian equivalent reflectivity (R) at λR = 388nm
Compute sensitivities, dN/dx, at 317, 325 and 340 nm for each of the retrieved parameters in (1) to form a 3 x 3 Jacobian matrix (K)
Invert K matrix to retrieve corrections Δxi: ΔSO2, ΔO3 and Δ(dR/dλ)
Update state vector by iteration, where xi=xi-1+∆xi
dR/dλ used to correct reflectivity at shorter channels: 317, 325 and 340nm
Notes: Description of the DSCOVR/EPIC SO2 Algorithm PI: Nick Kroktov
The DSCOVR/EPIC volcanic SO2 algorithm is a modified version of the heritage NASA Total Ozone Mapping Spectrometer (TOMS) 4-band algorithm, adapted to the EPIC wavelengths. The algorithm uses all four EPIC UV channels (centered at 317nm, 325nm, 340 nm, 388nm) to retrieve 4 parameters of the state vector (x): vertical column amounts of SO2 (assuming 13km height) and total O3, the Lambertian equivalent reflectivity at 388 nm (R), and its spectral dependence, dR/d. The algorithm relies on spectral differences in SO2 and O3 absorption cross sections to separate the two trace gases. SO2 is more absorbing than O3 at the shortest UV channel (317 nm), whereas O3 is more absorbing at the longer channel (325nm).
The retrieval is performed iteratively for each EPIC pixel with SZA < 75o. It starts with the climatological profile of O3 and zero SO2 and first computes Lambertian equivalent scene Reflectivity (LER) at 388 nm (R). This parameter remains fixed during the iterations. The algorithm then retrieves adjustments to the state vector: Δx =[ΔSO2, ΔO3, Δ(dR/d)] by matching measured and calculated sun-normalized backscatterd UV (BUV) radiances at shorter spectral channels (317,325 and 340nm). The sensitivities (Jacobians) associated with linear perturbations in SO2, O3 and R are pre-computed for each UV spectral band and stored in look-up tables, which are numerically interpolated for EPIC viewing geometry and state vector values at each iteration. This algorithm appears to have adequate sensitivity to detect moderate to large volcanic eruptions from L1 Lagrange point.
Max iterations = 3
Quit itrations when Min res325 = 0.001 ( N value)

## Slide 5
Forward Radiative Transfer Model (RTM)
LUTs:
O3 [Daumont et al., 1992] and SO2 [Bogumil et al., 2003] laboratory temperature dependent cross sections used to generate master LUTs
21 standard TOMS O3 profiles and SO2 profiles: 0, 5, 10, 50, 100, 150, 200, 250, 350, 450, 550, 650 Dobson Units
SO2 plume Gaussian vertical profile shape with a peak altitude of 13 km and a standard deviation ±2.0 km
EPIC instrument LUTs derived from master radiance tables using pre-flight measured EPIC spectral response functions centered at 317, 325, 340 and 388nm
TOMRAD RTM [Dave 1965] calculations are used to create hyperspectral radiance (master) Look-Up Tables for all geometries, LERs and O3 and SO2 profiles (LUTs)

## Slide 6
Solar Zenith Angle
EPIC Viewing Geometry
Viewing Zenith Angle
Relative Azimuth Angle

## Slide 7
EPIC SO2 Algorithm: Step 2
NM: Measured N= -100*log10(I/F), NC: Calculated N= -100*log10 (I/F)
dN/dSO2, dN/dR represent sensitivities of N vrt SO2 and Reflectivity.
Step 2 reduces false positive and negative SO2 artifacts due to spatial and temporal mismatch between 4 UV channels
that are not completely accounted for in Level 1B processing
Use Step 1 retrieved quantities (SO2, dR/dλ and R) as first guess
Apply 31 x 31 box smoothing to Step 1 O3 to obtain a smoothed ozone field for full disc image. Use smoothed O3 for calculating sensitivities dN/dSO2 and dN/dR
Invert 2x2 K matrix to retrieve corrections Δxi: ΔSO2 and Δ(dR/dλ)
Update state vector by iteration, where xi=xi-1+∆xi
Notes: Description of the DSCOVR/EPIC SO2 Algorithm PI: Nick Kroktov
The DSCOVR/EPIC volcanic SO2 algorithm is a modified version of the heritage NASA Total Ozone Mapping Spectrometer (TOMS) 4-band algorithm, adapted to the EPIC wavelengths. The algorithm uses all four EPIC UV channels (centered at 317nm, 325nm, 340 nm, 388nm) to retrieve 4 parameters of the state vector (x): vertical column amounts of SO2 (assuming 13km height) and total O3, the Lambertian equivalent reflectivity at 388 nm (R), and its spectral dependence, dR/d. The algorithm relies on spectral differences in SO2 and O3 absorption cross sections to separate the two trace gases. SO2 is more absorbing than O3 at the shortest UV channel (317 nm), whereas O3 is more absorbing at the longer channel (325nm).
The retrieval is performed iteratively for each EPIC pixel with SZA < 75o. It starts with the climatological profile of O3 and zero SO2 and first computes Lambertian equivalent scene Reflectivity (LER) at 388 nm (R). This parameter remains fixed during the iterations. The algorithm then retrieves adjustments to the state vector: Δx =[ΔSO2, ΔO3, Δ(dR/d)] by matching measured and calculated sun-normalized backscatterd UV (BUV) radiances at shorter spectral channels (317,325 and 340nm). The sensitivities (Jacobians) associated with linear perturbations in SO2, O3 and R are pre-computed for each UV spectral band and stored in look-up tables, which are numerically interpolated for EPIC viewing geometry and state vector values at each iteration. This algorithm appears to have adequate sensitivity to detect moderate to large volcanic eruptions from L1 Lagrange point.
Max iterations = 3
Quit itrations when Min res325 = 0.001 ( N value)

## Slide 8
Total Column Ozone
Step 1
Total Column Ozone
Step 2: Smoothed
EPIC SO2 diagnostic: Ozone

## Slide 9
EPIC SO2 diagnostic
SO2
O3 Smoothed
SO2

## Slide 10
EPIC SO2 diagnostic: Step 1 and Step 2 O3
O3 Step 2
O3 Step 1

## Slide 11
(x10-3)
EPIC SO2 diagnostic: LER(R) and dR/d𝜆
dR/d𝜆
LER

## Slide 12
EPIC shows SO2 Volcanic Plume Evolution

## Slide 13
10:04 UTC
11:52 UTC
08:16 UTC
Mount Etna, Italy Eruption
December 3, 2015

## Slide 14
00:55
02:43
04:31
06:19
Mount Aso Eruption 10/08/2016

## Slide 15
06:00
07:48
04:12
Mount Bromo, Java
January 2, 2016

## Slide 16
20:15
22:03
00:45
Mt. Bogoslof Eruption
March 8-9 2017

## Slide 17
01:23
02:28
03:34
Bogoslof Eruption
May 29, 2017

## Slide 18
Comparisons with OMI and OMPS

## Slide 19
DSCOVR/EPIC
10:04
OMPS TRU
11:05
Mt Etna, Italy
December 3, 2015

## Slide 20
Mount Aso, Japan
October 8, 2016
DSCOVR/EPIC
Aura/OMI
Suomi-NPP/OMPS
Not the same scale

## Slide 21
Pavlof eruption, Alaska
March 28 2016

## Slide 22
SO2 Mass = 3.9
SO2 Max = 27.3
Aura/OMI
05:52-07:33
DSCOVR/EPIC
07:48
Mount Bromo, Java
January 2, 2016

## Slide 23
March 28 2016 Pavlof eruption: Ash Index
OMPS AI
EPIC AI

## Slide 24
L1B Issues
Correlated Structures observed in SO2 background
Quasi-climatic structures observed possibly associated with clouds (e.g., southern hemisphere near

## Slide 25
05-28-2017 01:42
05-29-2017 01:23
05-30-2017 01:13
Step 1 O3 high intensity spot occurs on 3 images observed about the same time 1-day apart

## Slide 26
High bias around Earth Limb…. ?

## Slide 27
Product Status
Delivered source code to NCCS processing
Provided Marshall with list of volcanic cases for processing
Delivered product description and L2 data sample to Marshall
Working on ATBD draft. Deliver by the end of 2017
Working on journal publication of SO2 results from EPIC
Two abstracts submitted to 2017 Fall AGU meeting (EPIC session)

## Slide 28
Next steps
Deliver volcanic SO2 data and metadata to Langley ACDS
Improve retrievals for bright cloudy scenes
Adding more SZA and VZA nodes to LUTs
Improve retrievals for near Limb
Need continue EPIC operations to see larger volcanic plumes
Agung , Indonesia - ?