## Slide 1
EPIC L2 Cloud Product Updates
Yuekui Yang (GSFC)
Kerry Meyer, Gala Wind, Qilong Min, Anthony Davis, Steven Platnick, Daniel Holdaway
Alexei Lyapustin, Lazaros Oreopoulos, Zhibo Zhang
Thanks to:
David Duda, Patrick Minnis, Wenying Su
EPIC Science Team Meeting
03-04 October 2017 , Greenbelt, MD

## Slide 2: Cloud Product System
Cloud Mask
Cloud Optical Thickness
Effective Height/Pressure
EPIC L1B Products
Ancillary Data
EPIC L2 Cloud Products

## Slide 3
EPIC Channels Currently Used for Cloud Products
l (nm) | Dl (nm) FWHM | Purpose
317.5±0.1 | 1±0.2 | Ozone
325±0.1 | 2±0.2 | Ozone
340±0.3 | 3±0.6 | Ozone, Aerosols
388±0.3 | 3±0.6 | Aerosols, Clouds
443±1 | 3±0.6 | Aerosols
551±1 | 3±0.6 | Aerosols, Vegetation
680±0.2 | 2±0.4 | Aerosols, Vegetation, Clouds, O2 B-Band Reference
687.75±0.2 | 0.8±0.2 | O2 B-Band Cloud Height
764.0±0.2 | 1±0.2 | O2 A-Band Cloud Height
779.5±0.3 | 2±0.4 | O2 A-Band Reference, Vegetation

## Slide 4: EPIC L2 Cloud Product List
EPIC Cloud Mask
Oxygen A-band Cloud Effective Pressure
Oxygen A-band Cloud Effective Height
Oxygen B-band Cloud Effective Pressure
Oxygen B-band Cloud Effective Height
Cloud Optical Thickness – assuming liquid phase
Cloud Optical Thickness – assuming ice phase
Cloud Effective Temperature
Most likely cloud thermodynamic phase

## Slide 5: Current Status
Operational:
EPIC cloud product system has been integrated into the production line
Products will be released as soon as processing and checking is finished (within a month)
Publications:
Holdaway, D. and Y. Yang, 2016: Study of the Effect of Temporal Sampling Frequency on DSCOVR Observations Using the GEOS-5 Nature Run Results (Part II): Cloud Coverage. Remote Sens. 8(5), 431, doi:10.3390/rs8050431.
Meyer, K., Y. Yang, and S. Platnick, 2016: Uncertainties in cloud phase and optical thickness retrievals from the Earth Polychromatic Imaging Camera (EPIC), Atmos. Meas. Tech., 9, 1785-1797, doi:10.5194/amt-9-1785-2016.
Holdaway, D. and Y. Yang, 2016: Study of the Effect of Temporal Sampling Frequency on DSCOVR Observations Using the GEOS-5 Nature Run Results (Part I): Earth’s Radiation Budget. Remote Sens. 2016, 8(2), 98; doi:10.3390/rs8020098.

## Slide 6: EPIC L2 Cloud Product File Structure

## Slide 7: 1. Cloud Mask
T2
Cld LC
T3
T1
Clr HC
Clr LC
Cld HC
Test

## Slide 8: 2. Cloud Effective Height/Pressure
Cloud height retrieval with O2 absorption has been successfully applied to several missions, such as GOME, MERIS, POLDER, OMI, SCIAMACHY etc., as well as many other studies.
B-band
reference
A-band
reference
A-band
B-band
e.g., Daniel et al., 2003, Ferlay et al. 2010, Fischer and Grassl, 1991, Koelemeijer et al. 2001, , Kokhanovsky et al., 2005, Lindstrot et al. 2006, Stephens and Heidinger, 2000, Vanbauce et al. 2003, Vasilkov et al. 2008, Wang et al. 2008.

## Slide 9: Complexity of photon pathways
A- and B-band radiances are functions of:
Clear part
Cloudy part
Cloud fraction
Cloud optical depth
Atmosphere profile
Surface albedo
Sun-view geometry
Aerosol loading
Cloud top height
Cloud geometrical thickness
Cloud particle size and shape
Cloud phase
Cloud vertical distribution

## Slide 10: Mixed Lambertian-Equivalent Reflectivity (MLER) method
Variables:
Rabs: absorption channel radiance
Rref: reference channel radiance
Ac: cloud fraction
αs: surface albedo
αc: cloud albedo
Tabs : absorption channel transmittance
Tref : absorption channel transmittance
A pixel contains two Lambertian reflectors, the surface and the cloud;
Clouds are opaque; no photon penetration and transmission considered.
Two cloud effective pressure sets, one for A-band and the other for B-band, are retrieved by solving the equations through iteration.
Mixed Lambertian Equivalent Reflectivity (MLER) Model, e.g. Koelemeijer et al. 2001

## Slide 11: 3. Cloud Optical Thickness Retrieval
EPIC cloud optical thickness retrieval adopts a single channel method assuming a fixed effective radius.

## Slide 12: Uncertainties due to Single-Channel Retrieval
Distribution of single-channel COT retrieval errors w.r.t. two-channel COT-CER retrievals.
Meyer, Yang and Platnick, 2016, AMT

## Slide 13: Example: first granule from the production line (from 08GMT 08/18/2016)

## Slide 14: Cloud effective pressure

## Slide 15: A-band vs B-band pressure

## Slide 16: Cloud optical thickness

## Slide 17: COT retrieval ice vs liquid phase

## Slide 18: Most likely cloud phase
Clr Liq Ice UnD

## Slide 19: Comparison with Langley Composites
The Langley multi-sensor composites are produced by reprojecting GEO/LEO results (such as AVHRR, MODIS and GOES) onto the EPIC grids.
This dataset provides an independent source for EPIC cloud product verification.

## Slide 20: A large portion of the EPIC pixels are partially cloudy
How cloudy is cloudy?

## Slide 21: Comparison on global statistics
EPIC cloud mask can generally pick up pixels that are 30% to 50% cloudy.

## Slide 22: One complicated case in the day: 08 GMT
Composite
EPIC Cloud Mask

## Slide 23: Overland
EPIC Cloud Mask
Composite

## Slide 24: Over Ocean
EPIC Cloud Mask
Composite

## Slide 25: Difficulties in cloud detection over ice/snow
EPIC image time: 12/29/2015 18:27 GMT
Aqua MODIS time: 19:00 to 19:05 GMT

## Slide 26: Difficulties in cloud detection over ice/snow
0.47, 1.6, 2.1 µm as RGB
EPIC image time: 18:27 GMT
Aqua MODIS time: 19:00 to 19:05 GMT
But
MODIS has SWIR channels

## Slide 27: Cloud signal in EPIC A-band over different surface types

## Slide 28: Cloud signal in EPIC A- and B-bands over ice/snow
A-band Ratio
B-band Ratio

## Slide 29: Cloud Mask Using EPIC Oxygen A- and B-bands
MODIS time: 19:00 to 19:05 GMT
EPIC time: 18:27 GMT

## Slide 30: Cloud height comparison
☐ A-band Pressure (mean: 658 mb)
* Langley Composite (mean: 645 mb)
Cloud height comparison between EPIC A-band retrieval and the composite along Line 1100 (middle of image)
Modeling results of cloud height retrievals from EPIC A- and B-bands
SZA=VZA
Yang et al. 2014, JQSRT

## Slide 31: Cloud height comparison: A-band, B-band and composite
☐ A-band Pressure
+ B-band Pressure
* Langley Composite
EPIC effective cloud height are generally lower that the cloud height from the composites except in very high angles, which is consistent with the literature

## Slide 32: Cloud optical thickness comparison
☐ COT assuming liquid (mean: 8.9)
+ COT assuming ice (mean: 7.4)
* Langley Composite (mean: 9.5)

## Slide 33: Summary
EPIC cloud product system has been integrated to the production line; products will be releases as soon as processing is done.
Comparison with the GEO/LEO composites generated by the Langley group shows that 1) EPIC cloud mask can generally pick up pixels that are 30% to 50% cloudy; 2) EPIC effective cloud height are generally lower than the cloud height from the composites except in very high angles, which is consistent with the literature; 3) single channel cloud optical thickness retrieval provides valuable information.