## Slide 1: NIST Advanced Radiometer NISTAR
Dr. Steven Lorentz
James Briscoe
L-1 Standards and Technology

## Slide 2: Overview
Introduction
  NISTAR Description
  Objectives and Requirements
Data Products
Level 1 Data Issues
  Thermal Instability
  Operating Modes
Results
Future Work

## Slide 3: Introduction

## Slide 4: NISTAR Objective
The objective of NISTAR is to measure the solar reflected and Earth emitted irradiance along the Earth-Sun line.
An accurate measurement of the irradiance can help increase our understanding of the energy balance of the planet and human impact on climate change.

## Slide 5: NISTAR Channels
The irradiance is measured over four broadband channels:
Channel | Wavelengths | Description
Photodiode | 0.2 to 1.1 μm | UV-Vis-NIR
Band A | 0.2 to 100 μm | Total Irradiance
Band B | 0.2 to 4 μm | Total Solar Reflected
Band C | 0.7 to 4 μm | Near IR Solar Reflected
Notes: State the “why” for each channel – photodiode for calibration, band A for absolute radiation, band B to separate solar reflected portion, and band C to better understand the near IR region to help answer an open question in literature regarding this spectral band

## Slide 6: Irradiance Source Spectral Content
Blue: Estimate for solar reflected assuming Lambertian
Red: Earth thermal emissions
Two curves have almost equal integral
Notes: Integrals of two curve match, ~14 mW/cm2 sr

## Slide 7: NISTAR at Test Facility

## Slide 8: Radiometer Description
Active cavity radiometer with precision aperture.
Shutter is cycled open and closed and the power to maintain a nearly constant temperature in the cavity is measured.
More power = Less irradiance.
The irradiance is then computed by demodulating this square wave power signal to extract the optical power.
Apply a zero offset measurement using dark space calibration.

## Slide 9: Science Requirements
Absolute-calibrated daily mean irradiance or current measurements from all four channels
Must be able to provide measurements to determine total outgoing radiation of Earth in wavelength range of 0.2-100 μm with an accuracy of 1.5% or better.

## Slide 10: NISTAR Timeline
Feb 11th, 2015: Launch and NISTAR Power On
Feb 16th, 2015: First brief shutter opening
Mar 18th, 2015: First extended shutter opening
Apr 1st, 2015: Began editing ground processing software
Jun 7th, 2015: Lissajous injection burn
Aug 12th, 2015: First ground processing software release to NASA
Nov 9th, 2015: Transition to 30 minute autocycle
Jan 4th, 2016: Second ground processing software release to NASA

## Slide 11: NISTAR Timeline
May 10th, 2016: Transition to autocycle off
June 8th, 2016: Discovered temperature control anomaly which affected about a month of data total and four dark space calibrations
Sept 23rd, 2016: Transition to 4 minute autocycle
Oct 7th, 2016: NISTAR Ground Processing Software Version 1
Oct 24th, 2016: NISTAR Level 1 data public release
12 spacecraft safehold states, NISTAR requires at least two to four days to recover from each

## Slide 12: NISTAR Data Products

## Slide 13: NISTAR Level 0 Data
Level 0 data takes AppID sequential print data files, ephemeris, and attitude data and outputs data which has been:
Sorted into one file per Julian Day in chronological order.
Filtered to only contain data values which are within the defined limits.
Ensured not to contain two data points which are too close in time.

## Slide 14: NISTAR Level 1A Data
Science data is converted to engineering units.
Ephemeris and attitude data are used to determine what bodies are in the field of view.
Compute photodiode current and radiometer power from raw data.
Process calibration tables.
Outputs hdf files and text file inputs to Level 1B processing.

## Slide 15: NISTAR Level 1B Data Products
Level 1B data products are the daily, four hour, and four shutter cycle period averages of:
  Radiometer Irradiance: Demodulation of the radiometer power signal,
  Photodiode Current,
Along with the corresponding Geolocation data
Averages are only computed over data at nominal operating configuration, and only when enough data is present within the time bin

## Slide 16: Level 1 Data Issues

## Slide 17: Publicly Released Data
Last week the first NISTAR data was publicly released. This is not science-ready data:
Dark Space offsets not applied
Must be careful when comparing data from different operating modes
Other calibration parameters not applied.
Photodiode data good to go. Offset is well known, and not affected by mode changes.

## Slide 18: Next Data Release
The next data release will incorporate:
A finalized instrument state
Carefully applied offsets for past data to allow comparison across modes
Offset algorithm for data going forward
Calibration parameters
Data product of Earth irradiance daily, four hour, and four shutter period means
Calendar and metadata indicating good/bad data, and pertinent spacecraft events

## Slide 19: Uncertainty Sources
Level 1B Irradiance Averages
Radiometer Demodulated Power
Geolocation Data
Primary Aperture Area
Radiometer Power
Thermal Stabilization
Attitude Control
Ephemerides:
DSCOVR
Solar Lunar
Dark Signal Noise
Power Lost to Space
Calibration Data
Ground Calibration:
Filter Transmission
Receiver Responsivity
Dark Current
PTC Res. vs. T
Thermistor Res. vs. T
PD Spectral Resp.
Electronics Gain/Offset
On-Orbit Calibration: Dark Measurement
Filter Degradation
Receiver Responsivity
Filter Transmission
Quaternion Data
FOV/FOR
Jitter
Aperture Areas and
Separation
Relative Pointing between NISTAR and EPIC

## Slide 20: Uncertainty Budget Overview
Geolocation
Low uncertainties
Can tolerate 0.1° error
Calibration Data
Some are well defined
Some do not directly affect uncertainty
Responsivity needs more analysis
Thermal Stabilization
Increased shutter period
But still drifting
Now at short autocycle
Dark Signal Noise
Well understood
< 1% on Band A
< 2% on Band B
About 3-4% on Band C

## Slide 21: Thermal Stability

## Slide 22: Operations with Autocycle On
Shutters cycled open and closed
Measured irradiance from demodulating the noisy “square” wave power signal
Drifting of the signal due to external thermal effects are canceled out in demodulation
Relies on internal thermal equilibrium achieved before next shutter motion

## Slide 23: Original Configuration: 10 Minute Shutter Period
No Equilibrium

## Slide 24: Second Configuration: 30 Minute Shutter Period
Did it Reach Equilibrium?

## Slide 25: Second Configuration: 30 Minute Shutter Period
Only use second half of data from each shutter motion
Small slope remaining showing it was not fully at equilibrium
This effect does not cancel out after subtracting dark measurement
Estimated 1-5% error due to this remaining drift

## Slide 26: Work Arounds
Increasing shutter period further not practical:
  Earth signal would change significantly within a shutter period
  Thermal time constant would increase
Can the decay curve towards equilibrium be modeled to predict final stabilized value?
  Decay waveform not constant
  Extrapolation introduces additional error
  How can accuracy be quantified?

## Slide 27: Autocycle On Conclusions
Thermal instability prevents meeting accuracy requirement
Longer shutter period not possible
Thermal effects highly dependent on shutter period

## Slide 28: Second Configuration: Autocycle Off
Shutter remains open all the time
Always at thermal equilibrium internally
Vulnerable to external thermal effects
Needs more frequent dark space calibrations to maintain accuracy
Need some way to interpolate dark power measurements in between calibrations
Heat sink power should be a measure of external thermal variability

## Slide 29: RC1 Autocycle Off (Last 5)

## Slide 30: RC2 Autocycle Off

## Slide 31: RC3 Autocycle Off (Last 5)

## Slide 32: Receiver Servo Anomaly

## Slide 33: Autocycle Off Conclusions
Would need weekly or at most biweekly dark space calibrations
Operations concerns
Even still, Heat sink power may not be good enough interpolating function to meet accuracy requirement
Unresolved receiver servo anomaly

## Slide 34: Current Configuration: Autocycle On 4 Min Period
Thermal effects showed to be significantly dependent on autocycle period
Shorter autocycle period would decrease temperature swing during shutter motions
Preempt the problem
Limit on how short: must return to temperature setpoint between shutter motions

## Slide 35: 4 Min Autocycle

## Slide 36: 4 Min Autocycle

## Slide 37: Autocycle Comparison
30 Min Autocycle Dark Space Calibration Noise % |  |  | 
 | Band A: Total Channel | Band B: Solar Reflected | Band C: Near IR Solar Reflected
Dark Cal 15 | 0.89 | 2.03 | 3.29
Dark Cal 18 | 0.64 | 3.29 | 4.43
Dark Cal 21 | 0.67 | 2.08 | 6.02
Dark Cal 22 | 0.91 | 1.34 | 5.47
Dark Cal 27 | 0.56 | 2.15 | 5.66
4 Min Autocycle Dark Space Calibration Noise % |  |  | 
 | Band A: Total Channel | Band B: Solar Reflected | Band C: Near IR Solar Reflected
Dark Cal 37 | 0.12 | 1.23 | 6.45
Dark Cal 38 | 0.50 | 1.39 | 1.28
Dark Cal 39 | 0.53 | 0.51 | 1.64

## Slide 38: What Have We Gained?
Allows quicker dark calibrations
Earth scene does not change significantly within shutter period
Absolute noise increases, but
Noise on daily mean decreases due to statistics
Visibly improved waveform shape

## Slide 39: Results

## Slide 40: Long Term PD Current
June 17th 2015
11:13
Sep. 22nd 2015
10:35
Dec. 22nd 2015
11:15
Mar. 21st 2016
11:06
June 21st 2016
12:08
Sep. 21st 2016
11:15

## Slide 41: Seasonal Variability of Photodiode
Scaled to remove distance effects
Signal increases as SEV angle approaches 0 (opposition)
30% Peak to peak variability relative to mean

## Slide 42: Seasonal Variability of Photodiode
Scaled to remove distance effects
Subsatellite latitude can quantify the seasonal effect
30% Peak to peak variability relative to mean

## Slide 43: Daily Variability of Photodiode
More visibility of ice caps and more cloud cover leads to increased irradiance
Average current: 84.73 nA
Peak to peak: 19.89 nA (23.5% of avg)
Nov 19th – Nov 23rd, 2015
Africa land mass corresponds to peak photodiode current each day
Average current: 70.77 nA
Peak to peak: 23.15 nA (32.7% of avg)
Oct 29th – Nov 3rd, 2015

## Slide 44: Seasonal Variability of Total Channel Irradiance

## Slide 45: Seasonal Variability of Total Channel Irradiance

## Slide 46: Seasonal Variability of Total Channel Irradiance

## Slide 47: Band A 30 Min Autocycle Dark Measurements

## Slide 48: 4 Min Autocycle Daily Means
Blue: Demodulated Power
Red: Dark Calibration Power
Black: Interpolated Dark Power

## Slide 49: 4 Min Autocycle Irradiance

## Slide 50: Future Work

## Slide 51: Future Work
Live Session for finalizing parameters
Validate accuracy for 4 minute autocycle data
Get back to filling calibration tables
  Relative responsivities
  Filter degradation
Rev 2 software and data release
Collaborate with Level 2 science teams
Prepare for AGU Fall Meeting
Publish results

## Slide 52: Epilogue
Live Session Results

## Slide 53: Live Session Results
Very much improved waveform, signal squared up nicely in exchange for increased fast
noise, which is filtered out by demodulation. Accuracy requirement will be met.

## Slide 54: Backup Slides

## Slide 55: Modeling Decay Waveform
For this data set,
RC 2: Slopes of remaining drift varies from 9.5e-7 to 1.6e-6 (W/hr)
RC 3: Slopes of remaining drift varies from 1.3e-8 to 2.4e-7

## Slide 56: Exponential Fitting
Assume functional of form:
Constant term captures the final settling point of the curve
B, C define horizontal offset and rate of decay
B, C expected to be negative on open side and only C expected to be negative on closed side
Least squares fit over each half period

## Slide 57: Exponential Fitting (2)
Radiometer 1 during dark cal
Where T is time in hours, Rad is power in Watts, and D and E are applied offsets (fixed parameters)
A | 
B | 
C | 
D | 
E | 
A | 
B | 
C | 
D | 
E | 

## Slide 58: Exponential Fit Algorithm
Very sensitive to initial guesses
Subtract mean Time and max/min Rad power (parameters D and E)
Solve least squares of with A fixed to maximum (or minimum) power (Linear Least Squares) Then use B, C from this as initial guesses to second solution with A as a free parameter (Nonlinear Least Squares)
If diverges adjust B, C and retry

## Slide 59: Exponential Fit Results
 | Dark Cal 15 RC1 (C) | Dark Cal 15 RC2 (A) | Dark Cal 15 RC3 (B)
Dark Demod | 7.65778E-007 | 3.15092E-005 | 7.26365E-007
Earth Demod | 6.85616E-007 | 3.10008E-005 | 5.09570E-007
Demod Earth Signal | 8.01625E-008 | 5.08355E-007 | 2.16795E-007
Dark Demod Std | 6.46084E-009 | 1.11245E-008 | 1.08052E-008
Demod Noise Percent | 8.05967543 | 2.188337229 | 4.984070799
Demod Daily Mean Noise Percent | 3.29034872 | 0.89338493 | 2.03473838
Dark Exp Fit | 7.83557E-007 | 3.16513E-005 | 7.69493E-007
Earth Exp Fit | 7.03863E-007 | 3.11506E-005 | 5.52424E-007
Exp Fit Earth Signal | 7.96938E-008 | 5.00672E-007 | 2.17069E-007
Exp Fit Demod Std | 1.63874E-008 | 2.43461E-008 | 2.69870E-008
Exp Fit Noise Percent | 20.56301434 | 4.862693161 | 12.43246319
Exp Fit Daily Mean Noise Percent | 8.39481545 | 1.98518617 | 5.07553184

## Slide 60: Exponential Fit Results (2)
 | Dark Cal 27 RC1 (C) | Dark Cal 27 RC2 (A) | Dark Cal 27 RC3 (B)
Dark Demod | 7.57177E-007 | 3.14624E-005 | 7.15100E-007
Earth Demod | 6.75633E-007 | 3.09639E-005 | 5.03363E-007
Demod Earth Signal | 8.1544E-08 | 4.98441E-07 | 2.11738E-07
Dark Demod Std | 1.13021E-008 | 6.88325E-009 | 1.11473E-008
Demod Noise Percent | 13.86011855 | 1.380956121 | 5.26465335
Demod Daily Mean Noise Percent | 5.658369705 | 0.563772975 | 2.14928573
Dark Exp Fit | 7.69885E-007 | 3.16211E-005 | 7.58347E-007
Earth Exp Fit | 6.94690E-007 | 3.11288E-005 | 5.52231E-007
Exp Fit Earth Signal | 7.51953E-08 | 4.92239E-07 | 2.06116E-07
Exp Fit Demod Std | 1.98873E-008 | 2.55559E-008 | 1.73129E-008
Exp Fit Noise Percent | 26.44757248 | 5.191754983 | 8.399594902
Exp Fit Daily Mean Noise Percent | 10.79717625 | 2.119525096 | 3.429120259

## Slide 61: 4 Min Autocycle Demod

## Slide 62: 4 Min Autocycle Conclusions
Dark Space Calibration #37 Results
Dark Space Calibration # 37: 2016/270/20:15 – 20:45 |  |  | 
Channel | Band A: Total Channel | Band B: Solar Reflected | Band C: Near IR Solar Reflected
Earth Signal [nW] | 502 | 195 | 65
Dark Noise [nW] | 3.9 | 16.1 | 27.9
Est. Signal Noise % for Daily Mean | 0.12 | 1.23 | 6.45

## Slide 63: 4 Min Autocycle Conclusions
Dark Space Calibration #38 Results
Dark Space Calibration # 37: 2016/284/20:15 – 20:45 |  |  | 
Channel | Band A: Total Channel | Band B: Solar Reflected | Band C: Near IR Solar Reflected
Earth Signal [nW] | 450 | 274 | 63
Dark Noise [nW] | 15 | 26 | 5
Est. Signal Noise % for Daily Mean | 0.50 | 1.39 | 1.28

## Slide 64: 4 Min Autocycle Conclusions
Dark Space Calibration #39 Results
Dark Space Calibration # 39: 2016/298/20:15 – 20:45 |  |  | 
Channel | Band A: Total Channel | Band B: Solar Reflected | Band C: Near IR Solar Reflected
Earth Signal [nW] | 528 | 246 | 100
Dark Noise [nW] | 19 | 7 | 11
Est. Signal Noise % for Daily Mean | 0.53 | 0.51 | 1.64

## Slide 65: Earth Signal Power Total Channel (Scaled by Distance)
15% increase from March to July
Notes: Measurements taken during dark space calibrations, earth signal most accurate at these times as no interpolation is needed

## Slide 66: Earth Signal Power Total Channel (Scaled by Distance)
Variation is a result of complex interaction between Latitude (Seasons) and Sun-Earth-Vehicle Angle (Geometry)
Notes: Measurements taken during dark space calibrations, earth signal most accurate at these times as no interpolation is needed