## Slide 1: Monitoring the calibration of the DSCOVR EPIC V3 L1b product using MODIS and VIIRS as a reference
Conor Haney, David Doelling, Wenying Su, Rajendra Bhatt, Ben Scarino, Arun Gopalan
DSCOVR EPIC and NISTAR STM
October 6-8, 2020 virtual meeting

## Slide 2: ATO/DCC Ray-matching Overview
Grid both EPIC and MODIS/VIIRS pixels into a 0.25º grid cells from ±30º latitude
Identify MODIS or VIIRS granules within 15 minutes of an EPIC image
Spatially shift the EPIC image to best match the cloud features of the MODIS/VIIRS image based on R2
Match in viewing/solar geometry: ∆VZA<15º, ∆RZA<15º, ∆(Scat)<15º
Normalize by cosine SZA to remove SZA difference
Apply spatial homogeneity filter
Apply spectral band adjustment factor (SBAF) to take into account spectral response function differences
All-sky Tropical Ocean (ATO)
Ocean only
ATO-based SBAF
All ocean scene types, no glint
Pair 0.5º EPIC and MODIS grid cells
Deep Convective Cloud (DCC)
Land and ocean
DCC-based SBAF
MODIS/VIIRS 11 µm temperatures < 220K
Pair 0.25° EPIC and MODIS grid cells

## Slide 3
E7 image, uncorrected
E7 image, corrected
VIIRS-I1
R2 Field
East
North
Nominal navigation
Corrected navigation
Shift the EPIC image ±5 0.25º regions and find the shift that has the best R2 correlation between the EPIC image and the MODIS/VIIRS granule.
Navigation Correction Overview
Notes: - R2 field: blue is closer to zero, red is closer to 1

## Slide 4
V02
EPIC Image Shifts
Navigation has improved dramatically going from V02 to V03
Shift | V2 | V3
East-West | 31.8 ± 32.7 km | -11.5 ± 16.5km
North-South | 17.2 ± 19.7 km | 11.1 ± 15.2km
R2 | 0.841±0.01 | 0.833 ±0.03
V03

## Slide 5: Spectral Band Adjustment Factor (SBAF)
SCIAMACHY-based hyper-spectral radiances are convolved with the EPIC and MODIS/VIIRS channel SRFs using the NASA-LaRC SCIAMACHY SBAF tool (https://satcorps.larc.nasa.gov/cgi-bin/site/showdoc?mnemonic=SBAF)
Perform SCIAMACHY pseudo-radiance pair regression on same Earth scene-types used in ATO and DCC ray-matching
Apply resulting coefficients to MODIS/VIIRS radiances
E7
A1
I1
M5
Channel reflectance
NPP-VIIRS I1 0.1960
EPIC E7 0.1985
All-sky tropical ocean (ATO) mean and sigma spectra from 17352 SCIAMACHY footprints
Apply 2nd order fit to the 17352 pseudo I1 and E7 ATO reflectance pairs

## Slide 6
ATO
ATO
DCC
DCC
Linearly regress EPIC/NPP-VIIRS reflectance pairs on a monthly basis
Monitor the monthly EPIC gains over time and compute linear trend
EPIC E7/NPP I1 (0.64µm)
November 2016
EPIC E7/NPP I1 (0.64µm)
November 2016

## Slide 7: Combine the Aqua-MODIS, NPP and N20 VIIRS based EPIC calibration gains
Perform ATO and DCC ray-matching between analogous EPIC and Aqua-MODIS, NPP-VIIRS, and N20-VIIRS channels
Radiometrically scale both NPP-VIIRS C1 and N20-VIIRS C2 to the Aqua-MODIS C6.1 calibration reference
  Use ATO ray-matching, DCC invariant target (DCC-IT), and Libya-4 desert pseudo invariant calibration site (PICS) to transfer the Aqua-MODIS calibration to NPP-VIIRS and N20 VIIRS
Compare the monthly GOES-16 calibration gains from Aqua-MODIS and from NPP-VIIRS and N20-VIIRS that have been scaled to Aqua-MODIS
  To demonstrate the validation method
Compare the monthly EPIC calibration gains from Aqua-MODIS and from NPP-VIIRS and N20-VIIRS that have been scaled to Aqua-MODIS

## Slide 8
Coincident all-sky tropical ocean ray-matched (ATO-RM) radiance pairs
The Aqua-MODIS C6.1 B1 and NOAA20-VIIRS C2 I01 calibration timeline difference is 1.0634
Dec 2018, scaling factor =1.0671
NOAA-20 VIIRS I1 and Aqua-MODIS B1 ATO-RM 0.64 µm inter-calibration
Dec 2018

## Slide 9: Comparison of Aqua-MODIS/N20-VIIRS inter-calibration methods
Frequency
N20 VIIRS I01 Deep Convective Cloud (DCC) radiances, histogram all pixels with <205K
Ratio the N20-VIIRS and Aqua-MODIS DCC mode radiances to compute scaling factor
DCC Pixel Radiance (Wm-2µm-1sr-1)
All MODIS/N20 0.65µm scaling methods agree within 0.9%

## Slide 10
GOES-16/Aqua and GOES-16/N20 January 2020 scatter plot comparison
GOES-16/Aqua
Gain=0.1612
GOES-16/N20
Gain=0.1519
GOES16/N20 scaled to Aqua
Gain=0.1613
• The G16/N20 gain is 0.1519 and is -5.8% lower when compared to the Aqua gain of 0.1612
• After apply the N20/Aqua radiometric scaling factor, the Aqua and N20(scaled to Aqua) gain difference is +0.1%
• We can now use N20(scaled to Aqua) as the forward processing imager and maintain the Aqua calibration reference

## Slide 11: GOES-16 0.64µm ATO-RM gain comparison
G16 | unscaled | Scaled to Aqua
Aqua | 0.1617 | 0.1617
Terra | 0.1594 (-1.4%) | 0.1617 (0.0%)
NPP | 0.1610 (-0.4%) | 0.1612 (-0.3%)
N20 | 0.1521 (-5.9%) | 0.1617 (0.0%)
• The Aqua/N20 ATO-RM calibration difference was 1.0634 and very close to the 5.9% based on GOES-16
Compare dotted line (unscaled) with solid line (scaled to Aqua) with Aqua (solid black line)
• The GOES-16 calibration gain is within 0.3% of Terra-MODIS, NPP-VIIRS, and N20-VIIRS after radiometric scaling

## Slide 12: EPIC 0.68µm ATO-RM gain comparison
Compare dotted line (unscaled) with solid line (scaled to Aqua) with Aqua (solid black line)
E7 | unscaled | Scaled to Aqua
Aqua | 9.4492 | 9.4492
NPP | 9.5495 (+1.1%) | 9.4321 (-0.2%)
N20 | 9.1044 (-3.6%) | 9.4487 (0.0%)
• The Aqua/N20 ATO-RM calibration difference was 1.0634 (radiance based) and 1.0376 (reflectance based) and agrees with 3.6% based on EPIC reflectances
• The EPIC calibration gains are within 0.2% of NPP-VIIRS, and N20-VIIRS after radiometric scaling

## Slide 13
EPIC 0.68µm ATO-RM and DCC-RM gain comparison
E7 | ATO-RM | DCC-RM
Aqua B1 | 9.4492 | 9.3702 (-0.8)
NPP I1 | 9.4321 (-0.2%) | 9.4388 (-0.1%)
NPP M5 | 9.4512 (0.0%) | 9.4377 (-0.1%)
N20 I1 | 9.4487 (0.0%) | 9.4407 (-0.1%)
N20 M5 | 9.4561 (+0.1) | 9.4443 (0.0%)
• The EPIC calibration gains are within 0.2% based on either ATO-RM or DCC-RM methods, or based on I1 or M5 bands, except for Aqua-MODIS DCC-RM
Compare dotted line (DCC-RM) with solid line (ATO-RM)
NPP and N20 I1 bands shown
NPP and N20 have been scaled with Aqua

## Slide 14: EPIC 0.78µm ATO-RM and DCC-RM gain comparison
E10 | ATO-RM | DCC-RM
Aqua B1 | 1.4334 | 1.4175 (-1.1%)
NPP I1 | 1.4301 (-0.2%) | 1.4357 (+0.2)
NPP M5 | 1.4333 (-0.0%) | 1.4365 (+0.2%)
NPP M7 |  | 
N20 I1 | 1.4319 (-0.1%) | 1.4358 (+0.2%)
N20 M5 | 1.4327 (-0.0%) | 1.4364 (+0.2%)
N20 M7 |  | 
• The EPIC calibration gains are within 0.2% based on either ATO-RM or DCC-RM methods, or based on I1 or M5 bands, except for Aqua-MODIS DCC-RM
E10 scaled to Aqua-MODIS B1, since B2 saturates for bright scenes
NPP and N20 have been scaled with Aqua

## Slide 15
EPIC 0.55µm ATO-RM and DCC-RM gain comparison
E6 | ATO-RM | DCC-RM
Aqua B4 | 6.6510 | 6.6340 (-0.3%)
NPP M4 | 6.6726 (+0.3%) | 6.6810 (+0.5%)
N20 M4 | 6.6598 (+0.1%) | 6.7017 (+0.8)
• The EPIC calibration gains are within 0.8%
The Aqua/N20 radiometric scaling had a downward trend and is being looked at
NPP and N20 have been scaled with Aqua

## Slide 16: EPIC 0.44µm ATO-RM and DCC-RM gain comparison
E5 | ATO-RM | DCC-RM
Aqua B4 | 8.2356 | 8.2226 (-0.2)
NPP M4 | 8.4000 (+2.0%) | 8.4267 (+2.3%)
N20 M4 | 8.4256 (+2.3%) | 8.4433 (+2.5%)
• The EPIC calibration gains are within 2.5%
Note the increasing calibration drift with shorter wavelengths
NPP and N20 have been scaled with Aqua
The Aqua/N20 radiometric scaling had a downward trend and is being looked at

## Slide 17: Conclusions
EPIC was calibrated against the Aqua-MODIS C6.1 calibration reference
  NPP-VIIRS and N20-VIIRS were first radiometrically scaled to Aqua-MODIS
  EPIC calibration gains based on NPP and N20 were within 0.2% for bands 7 and 10
The ATO-RM and DCC-RM calibration methods were within 0.3% for EPIC/NPP-VIIRS and EPIC/N20-VIIRS
The table below contains the EPIC calibration coefficients by band, the ± provides the range of gains by calibration method or by reference sensor
There is a very slight calibration trend for EPIC shorter wavelength bands
The 2020 EPIC observations are consistent with the 2015-2019 observations
Band Pair | GM 2018 gains | ATO-RM gains | Gain range | ATO_RM/GM | Trend %/year
E5/A3 | 8.34e-6 | 8.2356e-6 | ±2.5% | -1.3% | 0.1 - 0.3
E6/A4 | 6.66e-6 | 6.6726e-6 | ±0.8% | +0.2% | 0.1 - 0.2
E7/A1 | 9.30e-6 | 9.4492e-6 | ±0.2% | +1.6% | 0.1
E10/A1 | 1.435e-5 | 1.4334e-5 | ±0.2% | -0.1% | <0.05