## Slide 1
The First Pandora 2006
CMOS Spectometer Basic square Box
Single Filter Wheel Custom Electronics BUT IT WORKED!
Hand wiring Off the shelf parts

## Slide 2
Pandora in Thessaloniki
The spectrometer was temperature copn

## Slide 3
NO2: Thessaloniki, Greece 2006
A view to the south from the hill above the Thessaloniki University Physics Department building on 15 July 2006 showing the pollution in the city and over the Mediterranean Sea with an almost cloud-free sky. The mild brown color is probably from the NO2 in the air above Thessaloniki.

## Slide 4
Pandora (blue circles), Brewer (red circles), and OMI (green circles)
The daily variation of C(NO2) in Thessaloniki, Greece, for 14 July to 24 July 2006

## Slide 5
NASA Goddard Work Detector
Annual average for day of the week diurnal behavior of C(NO2) at GSFC. The gray area around each line shows the mean value ± the standard error of the mean.

## Slide 6
Winter(December, January, February), spring (March, April, May), summer (June, July, August), and Fall (September, October, November). The gray area around each line shows the mean value ± the standard error of the mean.
Seasonal NO2 Cycle at GSFC

## Slide 7
and a head sensor on a sun tracker
What is PANDORA?
Pandora is a small spectrometer system, which we have been developing since 2006. We now have 50 Pandoras. It consists of …
a “miniature”
spectrometer
Measures sun and sky radiance from 270 to 530 nm in 0.5 nm steps with a 1.6o field of view. Products: NO2, H2O, O3, SO2, HCHO, and aerosol properties.
O3: 3 DU accuracy and 1 DU precision
NO2: 0.1 DU accuracy and 0.01 DU precision

## Slide 8
What does Pandora Measure ?
Green: No Filter
Blue: UV340 (Filter that blocks the visible light)

## Slide 9
Solar Irradiance Above the Atmosphere
280 nm
530 nm

## Slide 10
Knowing the Solar Spectrum, Remove Solar Spectral Features

## Slide 11
NO2: Traffic Light Problem
High time variability at GSFC observed on 14 and 24 May 2007 by Pandora and MFDOAS.

## Slide 12
NO2 as a GSFC Work Detector

## Slide 13
Air Quality and Ground Validation of Satellites:
Two Pandoras in Direct Sun & Sky-Scan Modes
Total Column every 80 seconds
Profiles every 20 minutes
O3
SO2
HCHO
BrO
NO2
H2O

## Slide 14
Pandora installation on a table
The installation is all weather and
requires little or no field operator intervention. Pandora needs 200 watts of A/C power and Internet access.
The Pandora optical head assembly schematic and photograph (inset). Filter wheel 2 (FW2) contains neutral density filters ND1 to ND4, 3 polarization filters, and an open hole. Filter wheel 1 (FW1) contains an open hole, opaque (dark current), and two UV bandpass filters U340 and BP300 (stray light reduction). The fiber optic cable feeds a small spectrometer in a weather proof box
What is Pandora?
A small spectrometer system measuring between 290 and 530 nm with 0.5 nm resolution

## Slide 15: Profiles of NO2 Compared with Aircraft Measurements Discover-AQ
NO2 profiles derived from Pandora direct-sun and MAXDOAS observations over Fresno, California on 18-Jan-2013
Comparison of Pandora retrieval to aircraft (P3B) measured NO2 profile (Fresno California).
Variation of Boundary Layer
NO2 Profile

## Slide 16
Pandora Measurements of Ozone Profiles Compared with O3 Balloon Sondes
Smith Point, Texas on Sept 18 and 26, 2013
Pandora O3 Profile
Balloon Sonde O3 Profile
Notice the profile agreement in the Troposphere

## Slide 17
Fitted Pandora slant column optical depths (blue) for a measurement on 22 July 2006
during the campaign in Greece (red). The left side shows the measurement with the 380-nm low pass
filter; the right side shows the measurement without filter. Note that the wavelength range 370– 380 nm
appears on both sides.

## Slide 18
The black legends give the final retrieved vertical column amounts for each
atmospheric absorber.

## Slide 19
Known Pandora Bugs
EFFECTS
Reduced Transmission
Reduced SNR
Variable Signal
False Diurnal Change
Main Goal of Pandora
Project
ELIMINATE BUGS
BEFORE TEMPO FLIES

## Slide 20
Day to Day Variability of Ozone in a Mountain Region

## Slide 21
Earth as a Planet: A view from the Moon

## Slide 23
Drawing of the DSCOVR Spacecraft located at Lagrange-1

## Slide 24
Lunar Transit with Music

## Slide 26
June
December
The View of Earth from Lagrange-1
Natural Color EPIC Earth images from June 6 and December 6, 2016 showing the field of view during the respective hemispheric summers.

## Slide 27
EPIC observed ozone from 23 November 2015 at 16:20 GMT showing the remnant of the Antarctic ozone hole.
Antarctic Ozone Hole Observed from Lagrange-1

## Slide 28
EPIC Ozone for US with high O3 on the east coast including NASA HQ
High Values on May 6, 7, and 8

## Slide 29
EPIC O3 for US with high O3 on the east coast including NASA HQ

## Slide 30
Pandora O3 for NASA HQ

## Slide 33
Pandora

## Slide 34
Pandora Ozone Compared to EPIC Ozone
Daily O3 data for EPIC (red) and Pandora (Grey) 2015 - 2016.
EPIC ozone data compared to Pandora retrievals at Boulder Colorado

## Slide 35
Computer Modelling such as the Merra-2 data assimilation model has become an essential tool for understanding the atmosphere.
EPIC and MERRA-2

## Slide 36
2
2
10
Locations of operating NASA Pandoras
1Colorado 4 Canada 2 Tenerife 1 New Mexico
10 GSFC 2 Boston 1 Houston 1 Taiwan
2 Langley 2 Finland 2 S. Korea 4 Argentina
New NASA Pandoras for 2016: nd VA
CCNY (NYC). Chesapeake Bay
Saint Louis MO Richmond VA
Boulder CO. Huntsville AL
Wallops VA Table Mtn, CA
6
2
Buenos Aires
Bariloche
Neuquen
Cordoba
Namibia
Helsinki (FMI)
Utrecht (KNMI)
2xBerlin Bucharest
Davos WRC
2x Innsbruck
2x Rome
Athens
GSFC
NASA-HQ
2 - LARC
Boulder
New Mexico
Houston
Mauna Loa
2-Tenerife
Australia
+5x Australia 2017
NASA PANDORAS AND ESA PANDONIA INSTRUMENTS
More than 40
2- Korea

## Slide 37: What is the Pandora System?
Pandora uses a symmetric Czerny-Turner spectrometer optimized for detection of trace gases in the 280 – 525 nm spectral range (0.5 nm resolution connected by a 400 micron fiber optic cable to an optical head (1.6O field of view) mounted on a high precision (0.01O) sun-sky tracker.
Primary Products
O3 and NO2 total column
O3 and NO2 Altitude profiles every 15 minutes
O3 from 0 to 50 km
NO2 from 0 to 10 km